BLE
(from espressif documentation)
Hasan Atakan Bedel

---
BLE Modes
- Connectable Scannable Undirected Mode
- High Duty Cycle Directed Mode and Connectable Low Duty Cycle Directed Mode
- Scannable Undirected Mode
- Non-connectable Undirected Mode

---
. BLE Broadcast Filtering Policy
- ADV_FILTER_ALLOW_SCAN_ANY_CON_ANY
  (Can be scanned and connected to any device (no white list)
- ADV_FILTER_ALLOW_SCAN_WLST_CON_ANY
- ADV_FILTER_ALLOW_SCAN_ANY_CON_WLST
- ADV_FILTER_ALLOW_SCAN_WLST_CON_WLST

---
Server And Client
Server(Slave,Peripheral) ---- Client(Master,Central)

---
Common Operations
- A client sends data to a server by writing data into the server. Both the Write Request and Write Command can be used to write an attribute value.
- However, a write Response is only prompted when a Write Request is used

---
Common Operations
A server sends data to a client by sending an Indication or Notification to the client. The only difference between an Indication and a Notification is that a
Confirmation is prompted only when an Indication is used. This is similar to thedifference between a Write Request and a Write Command.

---
Common Operations
- A client can also obtain data from the server by initiating a Read Request.
- For detailed information regarding the common operations between a server and a client, please refer to
  Core_V5.0, Vol3. Part F, Chapter 3.4 “Attribute Protocol PDUs”

---
More Info
- The common operations between a server and a client are achieved by using ATT PDU.
- Each device can specify its supported MTU, which is the maximum length of an ATT message. In ESP32 IDF, the MTU can be 23 - 517 bytes, and the total length of an attribute value is not limited

---
- If the length of the user’s packet is greater than (MTU-3), a Prepare Write Request is required to write data.
- Similarly, if the length of the packet is greater than (MTU-1), a Read Blob Request is required to read the remaining data.